## Slide 1: Guidance on Rational use of PPE for Covid-19 Management
Developed with input from MOH, WHO,CDC,IDI

## Slide 2: Introduction
This presentation summarizes WHO’s recommendations for the rational use of personal protective equipment (PPE) in healthcare and community settings, as well as during the handling of cargo.
In this context, PPE includes
  Gloves, Medical masks, Goggles or a Face Shield, and Gowns, as well as for specific procedures, Respirators (i.e., N95 orFFP2 standard or equivalent) and aprons.
This presentation is intended for those who are involved in distributing and managing PPE, as well as public health authorities and individuals in healthcare and community settings.
It aims to provide information about when PPE use is most appropriate.

## Slide 3: Examples of PPE for use in health care settings for COVID-19
Head cover
Head + hair
Goggle
Eyes
Nose + mouth
Gown
Face Mask
N95 Mask Face shield
Eyes + nose + mouth
Gloves
Hands
Nose + mouth
Apron
Body
Body

## Slide 4: Strategies to optimize the availability of personal protective equipment (PPE)

## Slide 5
Setting | Target personnel or patients | Activity | Type of PPE or procedure
Healthcare facilities Inpatient facilities Patient room | Healthcare workers | Providing direct care to COVID-19 patients. | Medical mask; Gowns, Gloves, Eye Protection (Goggles or Face shield) Gown
 |  | Aerosol-generating procedures performed on COVID-19 patients. | Respirator N95 or FFP2 standard or equivalent,Gown,Gloves, Eye protection, Apron
 | Cleaners | Entering the room of COVID-19 patients. | Medical mask, Gown, Heavy duty gloves, Eye protection (if risk of splash from organic materials (or chemicals), Boots or closed shoes
 | Visitors | Entering the room of a COVID-19 patient | Medical mask Gown Gloves

## Slide 6
Setting | Target personnel or patients | Activity | Type of PPE or Procedure
Other areas of patient transit (e.g., wards, corridors). | All staff, including healthcare workers. | Any activity that does not involve contact with COVID-19 patients. | No PPE required
Triage | Healthcare workers | Preliminary screening Not involving direct contact | Maintain spatial distance of at least 1 m. No PPE required
 | Patients with Respiratory symptoms. | Any | Maintain spatial distance of at least 1 m. Provide medical mask If tolerated by patient
 | Patients without respiratory symptoms. | Any | No PPE required
Laboratory | Lab technician | Manipulation of respiratory samples. | Medical mask, Gown, Gloves, Eye protection (If Risk of splash)
Administrative areas | All staff, including healthcare workers. | Administrative tasks that do not involve contact with COVID-19 patients | No PPE required

## Slide 7
Consultation room | Healthcare workers | Physical examination of patient with respiratory symptoms. | Medical mask, Gown, Gloves and Eye protection.
 | Healthcare workers | Physical examination of patients without respiratory symptoms. | PPE according to standard precautions and risk assessment.
 | Patients with respiratory symptoms. | Any | Provide medical mask if tolerated.
 | Patients without respiratory symptoms. | Any | No PPE required
 | Cleaners | After and between consultations with patients with respiratory symptoms. | Medical mask, Gown, Heavy Duty Gloves Eye protection (if of splash from Organic or chemical materials. Boots a or closed shoes
Waiting room | Patients with respiratory symptoms. | Any | Provide medical mask if tolerated. Immediately move patient to an isolation room or separate away from others. If this is possible, ensure spatial distance of at least 1m from other patients. No PPE required.
 | Patients without respiratory symptoms. | Any | No PPE required

## Slide 8
 |  | Activity | Type of PPE or procedure.
Community |  |  | 
Home | Patients with respiratory symptoms. | Any | Maintain spatial distance of at least 1 m. Provide medical mask if tolerated except when sleeping
 | Caregiver | Entering the patient’s room, but not providing direct care or assistance. | Medical mask
 | Caregiver | Providing direct care or when handling stool, urine or waste from COVID-19 patient being cared for at home. | Gloves, Medical Masks, Apron (If risk of splash)
 | Healthcare workers | Providing direct care or assistance to a COVID-19 patient at home | Medical mask, Gown, Gloves, Eye protection
Public areas (e.g., schools, shopping malls, train stations). | Individuals without respiratory symptoms | Any | No PPE required

## Slide 9
Setting | Category of person | Activity | Type of PPE
Ambulance or transfer vehicle | Healthcare workers | Transporting suspected COVID-19 patients to the referral healthcare facility. | Medical mask Gowns, Gloves, Eye protection
 | Driver | Involved only in driving the patient with suspected COVID-19 and the driver’s compartment is separated from the COVID-19 patient. | Maintain spatial distance of at least 1 m. No PPE required.
 |  | Assisting with loading or unloading patient with suspected with suspected COVID-19 disease. | Medical mask, Gown, Gloves, Eye protection
 |  | No direct contact with patient with suspected COVID-19 but no separation between driver’s and patient’s compartment | Medical mask
 | Patient with suspected COVID Cleaners | Transport to the referral healthcare facility. | Medical mask if tolerated
 |  | Cleaning after and between transport of patients with suspected COVID-19 disease to the referral healthcare facility. | Medical mask, Gown, Heavy duty gloves, Eye protection (if risk of splash from organic material or chemicals). Boots or closed work shoes

## Slide 10: Donning and Doffing of PPE

## Slide 11: Droplet precautions when handling Covid-19 cases
Single room
  if single rooms are not available, separating patients from others by at least 1m
Health care workers must wear appropriate PPE:
  Medical mask
  Eye protection (goggles or face shield)
  Gown
Patient to stay in the room (limited movement)
  If transport/movement is required, require the patient using a medical mask and use predetermined transport routes to minimize exposure for staff, other patients and visitors.

## Slide 12
Source: https://apps.who.int/iris/bitstream/handle/10665/251426/9789241549721-eng.pdf?sequence=1&ua=1

## Slide 14: Airborne precautions
(in the context of COVID-19)
Airborne precautions are recommended ONLY for aerosol generating procedures such as:
bronchoscopy,
tracheal intubation,
pressure on the chest during cardiopulmonary resuscitation may induce production of aerosol.
The following is required:
Single room with adequate ventilation:
natural ventilation with air flow of at least 160 L/s per patient or
in negative pressure rooms with at least 12 air changes per hour and controlled direction of air flow when using mechanical ventilation
PPE: contact + droplet
  Substitute medical mask for high-efficiency masks in room (N-95, or FFP2 or equivalent masks)

## Slide 15: N95 Mask Fitting – Do a seal check before you enter the room!

## Slide 16
THANK YOU!